## Slide 1: HVAC Basics
Bin Yan
HVAC – Heating, Ventilation, Air-conditioning

## Slide 2: HVAC Energy Consumption
Cooling 642 kWh/m2
Heating 623 kWh/m2
Electricity 414 kWh/m2
Annual Energy Use
>60%
A lab building on campus
32%
DOE numbers

## Slide 3: HVAC
HVAC – Heating, Ventilation, Air-conditioning
Temperature
Humidity
Pressure
Ventilation
68°F (20°C) and 75°F (25°C)
30% relative humidity (RH) and 60% RH
A slightly positive pressure to reduce outside air infiltration.
Rooms typically have several complete air changes per hour
Diagram of mechanical system on the blackboard

## Slide 4: Where?
Mechanical Room: Boilers, chillers, pumps, heat exchangers…
Air Handling Units (AHUs): heat, cool, humidify, dehumidify, ventilate, filter and distribute the air.
Room Controls: thermostats and Variable Air Volume (VAV) boxes
Pictures from http://www.learnhvac.org/

## Slide 5: In the mechanical room
Boiler
Chiller
Pictures from https://rfd-training.tac.com/docs/HVAC.pdf

## Slide 6: Heating
Also to radiators, terminal reheat, domestic hot water.
Pictures from https://rfd-training.tac.com/docs/HVAC.pdf

## Slide 7: Heating
Pictures from https://rfd-training.tac.com/docs/HVAC.pdf

## Slide 8: Cooling
Pictures from https://rfd-training.tac.com/docs/HVAC.pdf

## Slide 9: AHU – Air Handling Unit
Return air
Exhaust air
Outside air
Supply air
Where does air come from and go to?

## Slide 10: AHU
Damper
Heating/Cooling Coil
Fan
Sensor
Filter
What’s in an AHU?
Pictures from https://rfd-training.tac.com/docs/HVAC.pdf

## Slide 11: AHU - Economizer
Economizer mode: Using outside air for cooling rather than mechanical cooling.
Linked
Minimum in summer
More outside air in winter
55°F
Pictures from https://rfd-training.tac.com/docs/HVAC.pdf

## Slide 12: AHU – Heating and Cooling
dehumidification
55°F
Pictures from https://rfd-training.tac.com/docs/HVAC.pdf
Notes: The AHU SAT = 55 all the time

## Slide 13: Humidification
Why before the cooling coil?
Pictures from https://rfd-training.tac.com/docs/HVAC.pdf

## Slide 14: VAV
Two variables – Temperature & Air Volume
damper
The box you can see in the hallway.
IF temperature too high
First reduce reheat till fully closed
Then increase air volume
IF temperature too low
First reduce air volume till minimum
Then start reheat
Pictures from https://rfd-training.tac.com/docs/HVAC.pdf
Notes: Add labels
If statement

## Slide 15: Winter
Outside
Return
Mixed

## Slide 16: Summer
Outside
Return
Mixed
Cooled and dehumidified

## Slide 17: The Real World
Any difference? Anything wrong?
52°F

## Slide 18: The Real World
52°F
Chilled water is still used when outside air is far below 52F
Temperature increased after humidification.
Sensor error.
Separate control caused counteraction.

## Slide 19: What we have learned?
What’s in the mechanical rooms.
What happens in air handling unit.
How VAV works.
What can happen in the real world.
The system that ensures the thermal comfort.

## Slide 20: Thanks!
binyan@design.upenn.edu